Conference for Food Protection

2010 Issue Form

Internal Number: 036

Issue: 2010 III-006

Title:

4-501.19 Manual & Mechanical Warewashing Equipment, Wash solution Temp.

Recommended Solution: The Conference recommends...:

that a letter be sent to FDA requesting that section 4-501.19 be revised to remove the minimum wash solution temperature and be classified as a Core C item by removing the "Pf" and substituting "C" at the end of the section as indicated below AND requests that the Annex 3 entry for this section be amended as stated below.

4-501.19 Manual Warewashing Equipment, Wash Solution Temperature.

The temperature of the wash solution in manual warewashing equipment shall be maintained at not less than 43°C (110°F) a temperature to effectively remove visible soil. or the temperature specified on the cleaning agent manufacturer's label instructions. C Pf

Further, the Annex 3 reference to Manual and Mechanical Warewashing Equipment, Wash solution Temperature be revised to address the importance of controlling the variables that help remove soils from the wares or utensils during washing and rinsing to assure effective sanitizing. An example change by replacement of the existing section is as follows:

4-501.19 Manual Warewashing Equipment, Wash Solution Temperature.

The wash solution temperature is important for removing organic matter along with other variables. If the temperature is too low, the performance of the detergent may be adversely affected, e.g., animal fats that may be present on the dirty dishes would not be dissolved unless detergents are adjusted to work at lower water temperatures or other variables like power spraying, turbo washing, or heavy scrubbing are used. The manufacturer's label instruction should be consulted and followed for the correct application pertaining to cleaning agent. The items being washed should be visually cleaned by noting the absence of soil prior to sanitization.

The wash solution temperature in mechanical warewashing equipment is critical to proper operation. The chemicals used may not adequately perform their function if the temperature is too low. Therefore, the manufacturer's instructions must be followed. The temperatures vary according to the specific equipment being used.

It is the policy of the Conference for Food Protection to not accept Issues that would endorse a brand name or a commercial proprietary process.